## Slide 1: frameless ALOHA: analysis of the physical layer effects
Petar Popovski Cedomir Stefanovic, Miyu Momoda
Aalborg University
Denmark

## Slide 2: outline
intro: massive M2M communication
frameless ALOHA
  random access based on rateless codes
  noise and capture
summary

## Slide 3: the shape of wireless to come
R1: today’s systems
R2: high-speed versions of today’s systems
R3: massive access for sensors and machines
R4: ultra-reliable connectivity
R5: physically impossible
data rate
1
kbps
Mbps
Gbps
bps
10000
1000
100
10
R5
≥99%
R2
# devices
≥95%
≥99.999%
R4
≥90-99%
R3
≥99%
R1

## Slide 4: massive M2M
it will be billions, but how many?
  Ericsson figure is pointing to 50 billions
  others are less ambitious
massive variation in the requirements
  traffic burstiness/regularity
    smart meter vs. event-driven surveillance camera
  data chunk size
    single sensor reading vs. image
  dependability requirements
    emergency data vs. regular update

## Slide 5: defining massive M2M the total number of managed connections to individual devices is much larger than the average number of active connections within a short service period

## Slide 6: access protocols for massive M2M
massive M2M setup emulates the original analytical setup for ALOHA
  infinite population, maximal uncertainty about the set of active devices
difference occurs if the arrivals are correlated
time
…
event
…
…
short service period

## Slide 7: how to make protocols for massive access
predict the activation:
  account for the relations among the devices, group support, traffic correlation
control the activation
  load control mechanisms
our focus: improve the access capability of the protocols
  departure from “collision is a waste”
  put more burden on the BS

## Slide 8: observations on random access
useful when
  the devices have not interacted before
  the required flexibility is above a threshold
use with caution
  in a static setup , the devices “know each other”, and a better strategy (learning, adaptation) can be used
signaling, waste (error, collisions) may take a large fraction of the resources
  especially important for small data chunks

## Slide 9: frameless aLOHA or rateless coded random access

## Slide 10: slotted ALOHA
essentially part of all cellular standards
all collisions destructive
  only single slots contribute to throughput
memoryless randomized selection of the retransmission instant

## Slide 11: expanding ALOHA with SIC (successive interference cancellation)
users send replicas in several randomly chosen slots
  same number of replicas per user
  throughput 0.55 with two repetitions per user
frame of M slots
. . .
. . .
time slots
N users
E. Casini, R. De Gaudenzi, and O. Herrero, “Contention Resolution Diversity Slotted ALOHA (CRDSA): An Enhanced Random Access Scheme for Satellite Access Packet Networks,” Wireless Communica- tions, IEEE Transactions on, vol. 6, pp. 1408 –1419, april 2007.

## Slide 12: how SIC is done
each successfully decoded replica enables canceling of other replicas
user 1
user 2
user 3
time
slot 1
slot 2
slot 3
slot 4

## Slide 13: SIC and codes on graphs
new insight
  analogy with the codes-on-graphs
  each user selects its no. of repeated transmissions according to a predefined distribution
important differences
  left degree can be controlled to exact values, right degree only statistically
  right degree 0 possible (idle slot)
. . .
. . .
variable nodes
G. Liva, “Graph-Based Analysis and Optimization of Contention Resolution Diversity Slotted ALOHA,” IEEE Trans. Commun., Feb. 2011.
check nodes

## Slide 14: frameless ALOHA
idea: apply paradigm of rateless codes to slotted ALOHA:
  no predefined frame length
  slots are successively added until a criterion related to key performance parameters of the scheme is satisfied
. . .
. . .
N users
M slots

## Slide 15: frameless ALOHA overview
single feedback used after M-th slot
  M not defined in advance (rateless!)
feedback when sufficient slots collected
  - for example, NR < N resolved users lead to throughput of
time slots
. . .
. . .
. . .

## Slide 16: frameless ALOHA stopping criterion
a typical run of frameless ALOHA in terms of
(1) fraction of resolved users
(2) instantaneous throughput
heuristic stopping criterion:
fraction of resolved users
genie-aided stopping criterion:
stop when T is maximal

## Slide 17: analogy with the rateless codes
structural
  selection of transmission probabilities
operational
  stopping criterion based on target performance
controlling of the degree distribution
  in the simplest case all the users have the same transmission probability

## Slide 18: errorless case
all users transmit with the same probability distribution
  no channel-induced errors
slot access probability
b is the average slot degree
objective: maximize throughput by selecting b and designing the termination criterion

## Slide 19: asymptotic analysis
probability of user resolution PR when the number of users N goes to infinity
M is the number of elapsed slots
asymptotic throughput

## Slide 20: result of the AND-OR analysis

## Slide 21: non-asymptotic behavior

## Slide 22: termination and throughput
 | 50 | 100 | 500 | 1000
 | 0.83 | 0.84 | 0.88 | 0.88
 | 0.82 | 0.84 | 0.87 | 0.88
 | 0.75 | 0.76 | 0.76 | 0.76
 | 0.97 | 0.95 | 0.9 | 0.9
 | 2.68 | 2.83 | 2.99 | 3.03
 | 0.83 | 0.87 | 0.88 | 0.89
simple termination:
stop the contention if either is true
FR≥V or T=1
genie-aided (GA) termination
the highest reported throughput for a practical (low to moderate) no. of users

## Slide 23: average delay
the rateless structure provides an elegant framework to compute the average delay of the resolved users
average delay as a function of the total number of contention slots M
  the probability that a user is resolved after m slots is p(m)

## Slide 24: average delay example
slot access probability
  optimized for throughput maximization
asymptotic analysis
observations
  average delay shifted towards the end of the contention period
  most of the users get resolved close to the end
  typical for the iterative belief-propagation
  NB: we have not optimized the protocol for delay minimization
p(M) | T | M/N | D(M)/N
0.928193 | 0.874474 | 1.06145 | 0.928031

## Slide 25: noise –induced errors
plug in the noise
the link of each individual user has a different SNR
received signal in a slot
example
  if user 2 is resolved elsewhere and cancelled by SIC, the probability that slot j is useful is high
  situation opposite when user 1 removed by SIC, slot j less likely useful

## Slide 26: capture effect (1)
gives rise to intra-slot SIC in addition to inter-slot SIC
typical model for the decoding process
received power of user i
noise power
Received power of interfering users
capture threshold

## Slide 27: capture effect (2)
the capture effect boost the SIC
capture can occur anew after every removal of a colliding transmission from the slot
  asymptotic analysis significantly complicated
no capture effect
with capture effect
unresolved user
resolved user

## Slide 28: capture effect: example
narrowband system, valid for M2M:
Rayleigh fading
pdf of SNR for user i at the receiver
  long-term power control and the same expected SNR for every user

## Slide 29: asymptotic analysis (1)

## Slide 30: asymptotic analysis (2)
high SNR => low b/SNR
  throughput is well over 1!
  throughput decreases as the capture threshold b increases
low SNR => high b/SNR
  the achievable throughputs drop
  noise impact significant
target slot degrees are higher compared the case without capture effect
  the capture effect favors more collisions

## Slide 31: non-asymptotic results
confirm the conclusions of the asymptotic analysis

## Slide 32: summary
high interest for massive access in the upcoming wireless
  M2M communication
coded random access
  addresses the fundamental obstacle of collisions in ALOHA
frameless ALOHA
  inspired by rateless codes, inter-slot SIC
  nontrivial interaction with capture and intra-slot SIC
main future steps
  finite blocklength
  reengineer and existing ALOHA protocol into coded random access